TwinPact 6pin firewire to the VIDEO laptop
Audio input
plug it to L input

Presenter's laptop
TwinPact input select switch

VGA from speaker's laptop to TwinPact
RGB/VGA indicator

TwinPact VGA to the projector

VIDEO laptop

dvswitch laptop
(PAGE 2)

Set up Procedure:
1. Connect the VGA cable from the Presenter's laptop to the RGB IN on the back of the TwinPact.
2. Connect the VGA cable from the Projector to the RGB OUT on the back of the TwinPact.
   Note: This may vary slightly depending on the room. e.g. some rooms have fixed projectors with input at the speaker desk, others have a FOSDEM-provided projector which needs to be connected directly.
3. Connect the Firewire cable from the 6pin Firewire port(on the back of the TwinPact) to the Slave/TwinPact Laptop.
4. Have the speakers Resolution set to 1024x768 if possible.
5. Connect the TwinPact Power and turn it on.
6. Press the Input Select button until the RGB light is on.
7. Make sure the Slave Laptop is running (the lid can be closed) or the Master laptop will not be able to connect to the TwinPact.
8. Connect the Slave/TwinPact Laptop to the LAN.
9. Connect the Firewire to the camera.
10. Connect the Firewire from the camera to the Master/dvswitch Laptop.
11. Connect the Audio cable to the L input of the camera. If there are two audio inputs, use Input 1.
12. Connect the Master/dvswitch Laptop to the LAN.
13. Power up the Master/dvswitch laptop, let it boot, and activate the record function in dvswitch (“r” key).

Setup the speaker/presenter.
1. Attach the VGA cable from the Twinpact to the laptop of the presenter.
2. Go to the Master/dvswitch Laptop and verify that everything is ok. If the screen is not visible, ask the speaker to try a different resolution and/or refresh rate.
3. If there is a black border around the presenter's slides, press the overscan button on the twinpact remote to enable the overscan function.

Teardown at the end of the day:
1. Power down the master and slave laptops using the power button.
2. Gather up all equipment listed in “Contents of kit...” section for the current day and place in the box.
3. Bring the box to the info desk in the K building.

How to get HELP?
Don't Panic :)
1. Open an IRC client and connect to irc.freenode.net ( /server irc.freenode.net ). The Master/dvswitch laptop has Xchat installed.
2. Join channel #fosdem-video ( /j #freenode-video ).
3. Ask for help in the channel. There are many people in the channel who should be able to help.
4. If no one replies or you need urgent help, send an SMS to Holger(+32 496 132 631) or Wouter (+32 486 836 198).
INSTRUCTIONS FOR SETUP (Page 1)

When you visit the info desk in the K building, you should receive a kit with the video equipment for your room. Please verify that your kit has everything in the “Contents of kit” list for your current day of the week and time of day and any room number labels on your equipment match. You should also verify the contents of the kit before returning it to the info desk at night.

Contents of kit for setup Friday and teardown Sunday night:
1. master laptop and power supply
2. slave laptop and power supply
3. mouse
4. TwinPact and power supply
5. camera in a rigid case
6. camera tripod
7. 2 power bars
8. 2 VGA cables
9. 1 4-to-4 firewire cable
10. 1 4-to-6 firewire cable
11. Instructions for Setup
12. papers for making notes about video recording issues

Contents of kit for teardown Friday evening, setup and teardown Saturday, and setup Sunday morning:
1. master laptop and power supply
2. slave laptop and power supply
3. TwinPact (no power supply)
4. camera and camera case (no power supply)
5. Instructions for Setup
6. papers for making notes about video recording issues

What is a TwinPact?
The TwinPact is the device we use to capture the image from a Presenter's laptop as it goes to the projector. The device is connected between the speaker's laptop and the projector and seamlessly captures the image being displayed without interfering with the projector and laptop communications. A picture of the TwinPact front and back is on the setup diagram.

Find Video Team Documentation Online:

https://video.fosdem.org/2014/doc/

We need volunteers for reviewing video! Please talk to Wouter or Holger for more information.

If you didn't get your video team t-shirt when you picked up your box on Saturday morning, visit the info desk in the K building.
IF SPEAKERS DO NOT WISH TO BE RECORDED, PLEASE DO NOT RECORD THEIR TALKS.
Please do not harm kittens. Do not taunt Happy Fun Ball.
(Page 3)

Troubleshooting Guide:
1. Don't Panic
2. Verify that your cables are securely connected, and in the right order from the Set up Procedure:
  1. Are your input and output VGA cables connected to the right ports on the TwinPact?
  2. Is the camera connected to the master, and not the slave?
  3. Is the TwinPact connected to the slave, and not the master?
3. Make sure the presenter's laptop is in 1024x768, 60 Hz resolution for the projector output.
4. Is the TwinPact set to RGB?
5. Is the lens cover removed from the camera?
6. If you see a yellow exclamation mark on any inputs in dvswitch (including speaker laptop and presenter slides), verify that your camera is set to 48K for audio rate. How to do this varies between cameras – see the “How to get HELP?” section if your camera doesn't seem to make this available in a menu.
7. Try restarting X if you are not currently recording. (Ctl-Alt-Backspace)
8. Check the camera configuration:
  1. Make sure it's set to SD video (not HD)
  2. It should have 4:3 aspect ratio
9. If all else fails, get help.